## Slide 1: Impact induced hardening in dense suspensions
Pradipto, Hirokazu Maruoka and Hisao Hayakawa
(Yukawa Institute for Theoretical Physics, Kyoto University, Japan)
Present address (ALITECS)
Present address (OIST, Japan)
In Jamming, Rheology, and Granular Matter (July 9th, 2025) @YITP
Notes: This talk is presented on July 10th.

## Slide 2: Welcome message
Welcome to the YITP, Kyoto University.
YITP was founded in 1953 in commemoration of Hideki Yukawa being awarded the Nobel Prize.
Hideki was the first director, and I am 11th director.
Granular Physics is a minor field in this institute, but let us enjoy the meeting.

## Slide 3: Brief overview of this meeting
Granular physics is a matured field as a result of the effort in last 40 years.
Stefan Luding is a leader of this field.
Hayakawa and Takada recently published a Japanese-textbook on nonlinear rheology: non-equilibrium statistical mechanics of granular materials, which will be translated in Springer.
  Chapters 5-7 contains subjects in today’s meeting.

## Slide 4: Contents
Introduction
Simulation & theory
  LBM simulation
  Floating model in early stage
  Effects of elastic force
Experiment
Conclusion

## Slide 5: Contents
Introduction
Simulation & theory
  LBM simulation
  Floating model in early stage
  Effects of elastic force
Experiment
Conclusion

## Slide 6: Impact induced hardening
Impact induced hardening can be commonly observed in dense suspensions.
This is applicable to protective vests.
The mechanism of running on liquids is not “discontinuous shear thickening (DST)” but impact induced hardening.
http://youtube-video-download.info/video/EhdgkziFhrY

## Slide 7: Some exotic phenomena
Running on a liquid
A pool filled with non newtonian fluid
https://www.youtube.com/watch?v=TY0JeMyRCdY
A corresponding experiment by our group

## Slide 8: Some previous experiments
Waitukaitis and Jaeger, Nature 487, 205 (2012)
Egawa & Katsuragi, Phys. Fluids 31, 053304 (2019).

## Slide 9: Contents
Introduction
Simulation & theory
  LBM simulation
  Floating model in early stage
  Effects of elastic force
Experiment
Conclusion
See Pradipto & HH, PRF 6, 033301 (2021), Phys. Fluids 33, 093110 (2021) & PRE 108, 024604 (2023)

## Slide 10: Simulation
Lattice-Boltzmann method for suspensions (Ladd, 1994)
DEM for frictional grains (Cundall & Strack, 1971)
Free surface (Leonardi et al, 2014,15)

## Slide 11
Free-falling projectile simulation
Pradipto & HH,
PRE 108, 024604 (2023).
Notes: Pradipto & HH, PRE 108, 024604 (2023).

## Slide 12: Analysis
How can we understand the physics of impact?
How can we reproduce the trajectory of the projectile?
How can we understand and
For dry granular Krizou & Clark, PRL 124, 178002 (2020) predict
For impact in suspension Bassard et al (JFM 923, A38 (2021)predict

## Slide 13: Our analysis
We propose the floating model for an early-stage impact.
Equation of motion can be described by
The force only contain the buoyancy force and viscous drag force.
The drag force can be understood by the Stokes drag for partially filled case.

## Slide 14: Comparison of the floating model with the simulation
It works well!
For

## Slide 15: Effect of elasticity
The floating model cannot be used for late stage.
To get rebounds we need the elastic force.
This elastic force is enhanced by the force chain between the projectile and bottom boundary.
Pradipto & HH, Phys. Fluids 33, 093110 (2021)
Notes: Pradipto & HH, Phys. Fluids 33, 093110 (2021)

## Slide 16: Elastic force acting on the projectile without bottom boundary effect
The energy is totally dissipated at .
Pradipto & HH, PRE 108, 024604 (2023)
Notes: Pradipto & HH, PRE 108, 024604 (2023)

## Slide 17: Summary of simulation & theory
We can simulate the motion of a projectile in a viscous suspension.
The projectile motion can be understood by the floating model in early stage.
To get rebound the elastic force induced by percolating force chains is important.
There is elastic contribution even if there are no percolating force chains.
The spring between the body and foot is important to run on a liquid.

## Slide 18: Contents
Introduction
Simulation & theory
  LBM simulation
  Floating model in early stage
  Effects of elastic force
Experiment
Conclusion

## Slide 19: Experimental project (H. Maruoka)
Size of simulation is small (.
  Size of the container is small=> Unrealistic?
  Size of grains is large=> Non-Stokesian?
To clarify the role of inertia in the fluid motion, we have performed experiments of both large grains and cornstarch.

## Slide 20: Overview of experimental setup and picture

## Slide 21: Dynamical impacts on suspension 𝜙 = 0.56
𝝓 = 0.56
DI = 4amin = 12 mm
amax = 4/3 amin = 3.0 mm
𝛒I=7.57𝛒f = 7.8 g /cm3
10W = D = 144 mm W = 1 .15DI = 13.9 mm
H = 112 mm
h = 1.5, 3.0, 6.0, 9.0, 12, 18, 25, 38, 50 cm (N = 10 times for every height)
Namax = Namin = 338

## Slide 22
Solid line: sol. of floating model
23070960 ( 𝜙=0.56)
u0 = 1509 mm / sec
eff,I = 146 Pa∙s
𝜉 = 0.1282
eff,II = 144 Pa∙s
𝜉 = 0.9528
Z (mm)
t (s)
t (s)
t (s)
VZ (mm/s)
F (g∙mm/s2)
22
Experiment of high packing fraction, 𝜙 = 0.56.
0.000
0.002
0.008
0.010
0.000
0.002
0.008
0.010
0.000
0.002
0.008
0.010

## Slide 23
Fmax (g∙mm/s2)
u0 (mm/s)
u0 = 600 mm / sec
u0 =40401 mm / sec
u0 = 1707 mm / sec
A step around u0 = 1707 mm/sec may comes from the boundary effect?
Experiment of high packing fraction, 𝜙 = 0.53, 0.56.
eff = 60 Pa∙s
eff = 169 Pa∙s
2000 fps

## Slide 24: Experimental results
We prepare the initial fraction where 0.56 is the possible maximum fraction covered by water.
The resulting fraction after the impacts are and 0.56.
We focus on vs , which can satisfy the relation by the floating model.

## Slide 25: Effective viscosity and
Effective viscosity depends little on the density.
Unfortunately, the result on is inconsistent with the prediction of the floating model.

## Slide 26
Cornstarch
Water : cornstarch = 1 : 1.5
t (s)
VZ (mm/s)
u0 = 1272 mm / sec
Fmax ∝ u03/2
u0 (mm/s)
Fmax (g∙mm/s2)
The solid line: The solution of the floating model

## Slide 27: Summary of experiments
It seems that the floating model works well even for a suspension of large grains.
  vs can be explained by the floating model.
  vs cannot be explained by the model.
The effective viscosity little depends on the impact speed and the density.
The elastic force appears only in the late stage as the simulation suggested.
Not clear differences between large grains & cornstarch
Notes: Dense suspensions have large effective viscosities.

## Slide 28: Contents
Introduction
Simulation & theory
  LBM simulation
  Floating model in early stage
  Effects of elastic force
Experiment
Conclusion

## Slide 29: Conclusion
We have performed simulation for impact induced hardening.
Our simulation reproduces experimental results.
  Friction between grains is important.
Simulation suggests that impact induced hardening differs from DST.
Floating model works well in early stage even for experiments.
See Pradipto & HH, PRF 6, 033301 (2021), Phys. Fluids 33, 093110 (2021) & PRE 108, 024604 (2023) as well as H. Maruoka & HH, arXiv:2406.19202.

## Slide 30
Thank you for your attention.